## Slide 1
SWIFT real-time data flow
AQH or AQD
or Signature
GPS and IMU
(Microstrain or SBG Ellipse)
CT-1
Met
Airmar
or
Vaisala
or
3D sonic
Camera
CT-2
CT-3
optional
raw files onboard SWIFT
(Sutron Xpert SD card, directories by com port)
processed files onboard SWIFT
(Sutron Xpert SD card, directories by com port)
Dissipation rate profile (AQH)
or
current profile (AQD)
or
dissipation + currents (Sig)
serial
4 Hz or 1 Hz binary
or 8 Hz binary
Database of received telemetry on shore-side server
Download zip archives of hourly files: http://faculty.uw.edu/jmt3rd/SWIFTdata/DynamicDataLinks.html
Live map: http://swiftserver.apl.uw.edu/map
data collection in bursts of 512 s at 720 s intervals
duty cycle configurable from 1 to 5 bursts per hour
Matlab structure of telemetry data and plots
(local machine)
serial
25 Hz binary
serial
1 Hz ASCII
serial
1 Hz ASCII
serial
1 Hz ASCII
4 Hz NMEA
or 1 Hz SDI-12
or 10 Hz ASCII
serial
0.25 Hz jpg
wave spectra
directional coefs
bulk parameters
mean value
std deviation
mean value
std deviation
mean value
std deviation
mean value
std deviation
or
inertial dissipation
(3D sonic only)
n/a
first burst of each hour only:
combine processed results to single binary telemetry file for Iridium SBD transmission
**jpg from camera included once per day, at 2100 UTC only**
Matlab script compileSWIFT_SBDservertelemetry.m
which loops thru all the SBD files in the downloaded archive (as the working directory)
and reads individual binary files using the function readSWIFT_SBD.m
then plots the whole dataset using the function plotSWIFT.m

## Slide 2
SWIFT post-processing data flow
processed files onboard SWIFT
(Sutron Xpert SD card, directories by com port)
data collection in bursts of 512 s at 720 s intervals
duty cycle configurable from 1 to 5 bursts per hour
Matlab structure of all processed data and plots
(local machine)
improved and phase-resolved dissipation rate profiles (AQH)
directional profiles (AQD)
raw wave displacements
improved wave spectra (no slope bias)
reprocess_IMU.m or reprocess_SBG.m,
which calls readSWIFTv3_IMU.m and rawdisplacements.m and XYZwaves.m
reprocess_AQH.m which calls readSWIFTv3_AQH.m, dissipation.m and structurefunction.m
reprocess_AQD.m, which calls readSWIFTv3_AQD.m
time lapse video
Matlab script concatSWIFT_offloadedSDcard.m which builds
telemetry SBD files for all bursts (not just first each hour, as was done onboard),
and then calls compileSWIFT_SBDservertelemetry.m to loop thru all the SBD files
and reads the binary files using the function readSWIFT_SBD.m
then finally plots the whole dataset using the function plotSWIFT.m
AQH or AQD
or Signature
GPS and IMU
(Microstrain or SBG Ellipse)
CT-1
Met
Airmar
or
Vaisala
or
3D sonic
Camera
CT-2
CT-3
optional
raw files onboard SWIFT
(Sutron Xpert SD card, directories by com port)
Dissipation rate profile (AQH)
or
current profile (AQD)
or
dissipation + currents (Sig)
serial
4 Hz or 1 Hz binary
or 8 Hz binary
serial
25 Hz binary
serial
1 Hz ASCII
serial
1 Hz ASCII
serial
1 Hz ASCII
4 Hz NMEA
or 1 Hz SDI-12
or 10 Hz ASCII
serial
0.25 Hz jpg
wave spectra
directional coefs
bulk parameters
mean value
std deviation
mean value
std deviation
mean value
std deviation
mean value
std deviation
or
inertial dissipation
(3D sonic only)
n/a

## Slide 3
Notes: all Matlab functions in ‘SWIFTcodes’ Dropbox folder
contact jthomson@apl.uw.edu for access
submit revisions to ‘beta’ subfolder, archive in ‘old’ folder
.prj files and ‘codegen’ subfolder are C++ conversions (used onboard)
Other codes (separate from data flow):
timeaverageSWIFTdata.m makes longer ensemble (burst) averages
SWIFTdirectionalspectra.m estimates average directional spectra
MEM_directionalestimator.m subroutine
polarPcolor.m subroutine
wavenumber.m solves dispersion in intermediate depth
concatSWIFT_SBDemailattachments.m is for email SBD usage (backup)
readSWIFTv3_ACS.m reads raw CT data (in ‘ACS.dat’ files)
readSWIFTv3_PB2.m reads raw Met data (in ‘PB2’ files), includes GPS
SWIFT_breaker_detection.m scores images for breaking waves
see ‘ImageProcessing’ subfolder
SWIFT data structure fields in Matlab (results by burst):
SWIFT.uplooking.tkedissipationrate: vertical profiles of turbulent dissipation rate in W/kg (= m^2 / s^3)
SWIFT.uplooking.z: depth bins, in meters, for the tke dissipation rate profiles. wave-following reference frame
SWIFT.downlooking.velocityprofile: vertical profiles of horizontal velocity magnitude, in m/s, relative to the float (not corrected for drift)
SWIFT.downlooking.z: depth bins, in meters, for the velocity profiles
SWIFT.winddirT: true wind direction FROM, in degrees CW relative to North
SWIFT.winddirTstddev: standard deviation of true wind direction, in degrees
SWIFT.windspd: wind speed, in m/s, at 1 m height above the wave-following surface
SWIFT.windspdstddev: standard deviation, in m/s, of wind speed
SWIFT.time: UTC timestamp in MATLAB datenum format (serial days since 0 Jan 0000)
SWIFT.date: human readable date as day, month, year
SWIFT.airtemp: air temperature, in deg C, at 1 m height above the wave-following surface
SWIFT.airtempstddev: standard deviation of air temperature, in deg C
SWIFT.sigwaveheight: significant wave height, in meters
SWIFT.peakwaveperiod: peak of period orbital velocity spectra (note convention is usually wave height spectrum)
SWIFT.peakwavedirT: true wave direction FROM, in degrees CW relative to North
SWIFT.wavespectra.energy: wave energy spectral density, in m^2/Hz, as a function of frequency
SWIFT.wavespectra.freq: spectral frequencies, in Hz
SWIFT.wavespectra.a1: normalized spectral directional moments
SWIFT.wavespectra.b1: normalized spectral directional moment
SWIFT.wavespectra.a2: normalized spectral directional moment
SWIFT.wavespectra.b2: normalized spectral directional moment
SWIFT.lat: latitude in decimal degrees
SWIFT.lon: longitude in decimal degrees
SWIFT.watertemp: water temperature, in deg C, at 0.5 m below the surface
SWIFT.salinity: water salinity, in PSU, at 0.5 m below the surface
SWIFT.puck: three color channels of a WetLabs puck flourometer
SWIFT.driftdirT: drift direction TOWARDS, in degrees True (equivalent to "course over ground”)
SWIFT.dirftspd: drift speed in m/s (equivalent to "speed over ground")
Raw (burst) file naming convention is SWIFTXX_ZZZ_ddMonYear_HH_BN.dat
where XX is the buoy serial number, ZZZ is the sensor, ddMonYear is the date,
HH is the hour (UTC), and BN is the burst number within that hour (1 to 5).